## Slide 1: On the Borderline between Target Management and Debugging
Martin Oberhuber, Wind River Systems

## Slide 2: A Simple Approach
Target Management prepares the target connection(s) and launches the debugger, such that a debugger can take over on an abstract connection.
Target Management | Debugger
Launching: does everything to create or find a context to debug (Process, …) | Takes over once the context is known
Setup board properties, access control, target connections and protocols | Deals with an abstract debugger connection
Loads and Resets target systems | Handles symbol files for loaded modules on attached contexts
Stores target specific properties (per target connection) | Stores breakpoints and options (per Launch)

## Slide 3: But is really everything so clear?
Debuggers can be very vendor specific.
  Should they “Launch themselves”?
  Does an abstract debugger connection make sense?
  Does it make sense to deal with hardware specifics like board layout and CPU in target manager?
  Resetting a target can be complex on JTAG
Attach to the Target vs. Attach to a context
  When debugger attaches to the Kernel, all contexts are at its disposal
  Debug View can show same things as a TM view

## Slide 4: And there are grey zones…
Cross-mounted file systems between host and target
  Used by TM for “downloading” and launching
  Used for Debugger Symbol File Loading (Object Path Mappings)
  TM may know how to initialize path mappings automatically
Kernel Objects View
  Exist outside debugging context
  But debugger symbol info may be needed to fill it
Target Groups
  Set up and managed by TM
  But debugger may want to do synchronous run control

## Slide 5: TM can help the Debugger
If we agree on interfaces and APIs…
TM can provide a pluggable abstract debugger connection
  IWRDebuggerBackend
TM can provide connection-specific storage for debugger options
  JTAG scan chain, board layout
  Options that should be valid for multiple Launches
  The connection-specific data store could be passed to the debugger in the Launch (since a connection reference needs to be stored in the Launch anyway)

## Slide 6: TM should be optional
Local host - native connections don’t need TM
  Simple connection, no properties, no download, no reboot
Platform could provide “null” implementations of TM features…
  To be extended by TM plugins
…or debuggers could search for TM extensions themselves.
So, one side of the border could be “Anything that is needed by local host - native debugging cannot belong to TM”